Wireless Podium Gooseneck Microphone  Using the MX412SE

Or the MX418SE

כך תפעילו מיקרופון SHURE   בעל צוואר גמיש שחור

באורך 30  או 45 ס"מ מותקן על דוכן. החיווט במעבר בלוח הדוכן אל החלל הפנימי שלו, השידור מבוצע באמצעות משדר אלחוטי רגיל מכל אחת מהסדרות שלנו 
חבוי בדוכן ומקלט תואם בהישג טווח שידור רגיל. הגרסה הקלהBLXR    לשימוש מקצועי,
ובמערכות מתקדמות  QLXD  ULXD ניתן להצפין את השידור והקליטה לצרכי אבטחת מידע.

כל מה שנדרש זה מיקרופון כיווני 184R או 185R עם צוואר MX412SE   או MX418SE

טבעת חיזוק 8264A65 שתוברג אל בסיס המיקרופון מתחת ללוח הדוכן,

ומחבר  TA4F  =  WA330חלופי, בהתקנה לפי ההוראות המצורפות בעמוד הבא – כאן למטה.

ומערכת אלחוט טובה מבית SHURE

נשמח לספק לכם אותם וכל מידע נוסף שביכולתנו לעזור בתחום זה

התמונה להמחשה  //   זווית התצוגה בגלל אילוץ העמוד  //  מתאם הפנטום

Wireless Podium Gooseneck Microphone  Using the MX412SE

Or the MX418SE

30 OR 45 CM

LONG

PASS THE WIRE VERTICALLY

REPLACE THE CONNECTOR

WITH # WA330.

טבעת זו יש לבקש בנפרד

Receiver  BLXR

QLXD  ULXD

Location within eye sight

# PROCEDURE

Cut the current TA4F connector and shorten the MX412SE’s cable to the desired length and install a new Switchcraft TA4F connector wired as shown.  (This connector is available from Shure as part # WA330.)  Plug the connector into the bodypack transmitter.

PARTS NEEDED      65B8264 Mounting Ring

One MX412SE or MX418SE gooseneck microphone

And one WA330 Switchcraft TA4F connector                     חובה לשים לב להוראות ולפעול כך:

NOTE: In late 2006, Shure began adding a TA4F connector to the MX412/SE and the MX418/SE. This change provides an improvement in RFI resistance. However, this TA4F connector is crimped and is wired with the cable shield NOT connected to pin 1. This TA4F must be removed and replaced by the WA330, following the instructions above, in order to use the MX412/SE or MX418/SE as a wireless gooseneck mic.

One Shure wireless system, with bodypack transmitter having 4-pin audio input connector

# Text boxes

TA4F CONNECTOR

(AS SEEN FROM REAR)

SHIELD

BLACK

(Connect to Pins 3 & 4)

RED

MX412SE

GOOSENECK  MICROPHONE

(Without preamp)

TA4F CONNECTOR

THREADED BASE OF MIC GOOSENECK

SHOCKMOUNT

(INCLUDED)

SHOCKMOUNT ADAPTER

(INCLUDED)

Cable is changed from Side Exit to Bottom Exit following instructions in User Guide.

Shure bodypack transmitter with 4-pin input connector

RF SIGNAL TO RECEIVER BLXR QLX

MOUNTING FLANGE

(Part # 65B8264 - not supplied) INVERTED

This would slide up the Shock mount 
  Adapter to hold the microphone in place so
 it cannot be pulled out of the Shockmount